## Slide 1
Weekly Review
By Omar Zreika (for Master Thesis in Energetic Physics
Last update:
18.05.2024
Mass spectrometer FOR Measurement of Heavy Metal Residuals in Municipal WASTE Incineration after Flue Gas Filtering

## Slide 2
. Working Principle .
1. Ionization
2. Acceleration
3. Deflection
4. Detection
07.05.2024
Slide 2

## Slide 3
. Asmaa Report .
Goal: Obtain a 0.2 Tesla
Result: Failed
Why!?
Reason: Using of helmoltz coil (weak)
Unknown Permeability
07.05.2024
Slide 3

## Slide 4
. Electromagnet .
The ferromagnetic core “μ”
The number of turns “n”
The electrical current “I”
Achieve a 0.2-0.25 Tesla
B: magnetic field in Tesla
μ: permeability in Henry per Meter
n: number of Turns per Meter
I: electrical current in Ampere
B = μnI
Our Goal
07.05.2024
Slide 4

## Slide 5
. Alibaba .
Pure iron is the best option for a high permeability compared to the air (relative permeability)
Alibaba best result:
10 pieces , purity 99.5%, shipping 82$, need annealing 70$ to reach 25000 relative permeability
Aliexpress:
Iron purity 99.9% but no data sheet
07.05.2024
Slide 5

## Slide 6
. Annealing .
Is it possible?!
Is it easy?!
Annealing process is to rise the relative permeability of the iron:
Temperature: 800-900 °C
Time of heating: 1hour per inch
Cooling rate: 1-2°C per hour
We need a programmable furnace
07.05.2024
Slide 6

## Slide 7
. Simulation .
COMSOL multiphysics
We should learn How (×3):
How to install the program
How to use the program
How to make the coil simulation
This will help us to know:
The best shape of the coil
The best number of turns
The strength of the magnetic field
07.05.2024
Slide 7

## Slide 8
. The detector .
We can’t do the test!!
If the electromagnet isn’t ready
We can’t do the test for the detector and know how to get the samples
We must hurry…
07.05.2024
Slide 8

## Slide 9
Slide 9
. Permeability .
In Electromagnetism, permeability refers to a material’s ability to concentrate magnetic fields compared to the empty space,
and symbolized by μ
It tells you how easily a material gets magnetized
It’s measured in Henry per meter (H/m)
Soft Iron
Wood
focuses and amplify magnetic fields
doesn’t affect the magnetic fields

## Slide 10
. Annealing II .
The Temperature affects the permeability:
( 800 to 900°C is the best )
The purity of the metal affects the time of the annealing:
( impure metals take more time than the pure ones )
The size affects the time of the annealing:
( The smallest the metal size, the smallest the time needed )
Slide 10

## Slide 11
. Annealing III .
A programmable furnace is needed for the annealing process
Two critical Specifications:
Can rise the temperature up to 850°C
Have a control panel to determine the time and the temperature of the annealing process
Heat treatment
Slide 11

## Slide 12
. Annealing III .
We need to clean the iron rod surface with a solvent (acetone or ethanol) to remove any dirt
Oxygen can react with iron at high temperature so we need to use an inert gas (nitrogen) to minimize the oxidation
We should purge the furnace with the inert gas about 10-15 min before introducing the iron rod
A continuous flow rate of the inert gas during the annealing process is recommended
We place the iron in the furnace and gradually rise the temperature to 850 °C, and hold it about 1 hour, we let it cool slowly and naturally while the furnace is closed
Slide 12

## Slide 13
. Purification .
Copper Case
e-
e-
Cu2+
Cu2+
Cu2+
Cu
Cu2+
Cu
CuSO4 Solution
Impure Copper
( Anode )
Result: Good
Pure Copper
( Cathode )
Slide 13

## Slide 14
. Purification .
Iron Case
e-
e-
Fe2+
Fe2+
Fe2+
Fe
Fe2+
Fe
FeSO4 Solution
Result: Bad
Impure Iron
( Anode )
Impure Iron
( Cathode )
Slide 14

## Slide 15
. Simulation II .
We successfully installed
COMSOL multiphysics
The program still need time to understand
how it works
If so, we can move on to make our coil simulation for the strength of the magnetic field
Slide 15

## Slide 16
Wipe down the iron rod with ethanol
Purge the nitrogen gas in the furnace
Turn on the furnace and set it to somewhere between 800 and 850 °C
Put the iron rod in a clay pot
Keep purging the nitrogen gas during all the annealing process
Place the iron rod inside the furnace carefully using gloves and tongs
Once it reaches the target temperature let the iron sit there for about one hour
Turn off the furnace
Let the furnace closed so the iron can be cooled slowly
Slide 16
. Annealing IV .
Annealing Process

## Slide 17
Muffle furnace advantages: Controlled environment: It prevents oxidation of the iron during annealing, which is important for magnetic properties. Uniform heating: Ensures consistent results in terms of microstructure and permeability. Precise temperature control: Allows for optimal annealing for permeability.
Slide 17
. Annealing V .