## Slide 1: Sustainable Waste Management in Saudi Arabia
Recycling and Biogas Utilization for Household Waste

## Slide 2: Content
Sorting of 1000 tons waste / day (as diala project)
Recyclable Material: 300 tons / day: Recycling to Plastics spheres
Biogas Production from 500 tons organic waste / per day
Incineration of 200 tons refused waste / day with electrical power generation: 4 blocks of the NLAP-2MW IPP (consumes 4x50 tons/day refused waste)
Our Reference Project: Mobile Pilot Plant in Lebanon (Waste Sorting – Biogas Production – Refused Waste Incineration with Electrical Power Generation)

## Slide 3: Introduction
Current Waste Management Challenges in Saudi Arabia
Rapid urbanization and population growth have led to a significant increase in waste generation.
Saudi Arabia produces approximately 15 million tons of waste annually, with per capita waste generation ranging between 1.5 to 2.5 kg/day.
Our objective is to treat 1000 tons of household waste per day, recycle it, produce biogas and the rest gets into Burning Process

## Slide 4: Waste Management
We have established:
Small-scale waste management plant. efficiently handles approximately 500 kilograms of household waste per day.
This facility is designed to treat household waste
Extract organic materials for a biogas digester, which then converts the waste into natural gas.
The entire process operates on a land area of about 2800 square meters.

## Slide 5
It is also characterized by its ability to sort continuously or intermittently daily.
The plant consists of:
A large tank for household waste.
A cutting and bag-opening area.
An automatic conveyor to move the waste.
Barrels designated for sorted materials.
Personal protective equipment, cleaning, and lighting equipment.
The sorting plant requires 7 workers to operate, distributed as follows:
One worker to fill the main barrel
One worker to cut and open the bags
Four workers to sort the waste: the first and second to separate paper, metals, and glass, and the other two to separate plastic and non-recyclable waste.

## Slide 6: Our Proposed Solution
We have conducted comprehensive studies for a waste management plant capable of processing 1000 tons of waste per day. (as diala Project)
Based on our findings, the complete waste management cycle for 1000 tons requires a land area of 50,000 square meters.
This facility will efficiently handle the waste treatment process, ensuring sustainable and effective waste management solutions.

## Slide 9: Our Power Plant

## Slide 13: Thermal treatment: incineration

## Slide 15: Proposed Solution
Incineration of 200 tons/day
of refused waste with electrical power generation
4 blocks of the NLAP-2MW IPP
(consumes 4x50 tons/day refused waste)

## Slide 23: Proposed Solution
The percentage of organic waste in municipal solid waste can vary by region and the type of waste, but a common average figure is around 40-50%.
Then how many anaerobic digesters and how much is the radius and height of each one to digest 500 tons of organic waste?

## Slide 24: The Project Design
To process 500 tons of organic waste per day, we would need:
5 anaerobic digesters.
Each with a diameter of 25 meters and a height of 12 meters.
A land of 120,000 x 280,000-meter square for the 5-digester system.
280,000-meter
120,000-meter
Digester 1
Digester 2
Digester 3
Digester 4
Digester 5
Inlet 2
Inlet 1
Inlet 5
Inlet 4
Inlet 3
Outlet 1
Outlet 2
Outlet 3
Outlet 5
Outlet 4
Biogas pipe
Biogas pipe
Biogas pipe
Biogas pipe

## Slide 26
Digester
Inlet
Outlet
Slurry Outlet
ground
Gas chamber
Biogas Outlet
People