## Slide 1
Introduction: Aspirin or Acetylsalicylic acid (ASA) is one of the first drugs to come into common usage, still widely used around the world with approximately 40,000 tonnes produced globally each year. Aspirin is an ingredient in many proprietary analgesic and cold/flu preparations. It is also used for the prevention of cardiovascular disease and there is growing work on its role in the prevention and management of cancer. Aspirin ( C9H8O4) remains on the World Health Organization’s Model List of Essential Medicine (21st List 2019) both for its use in pain control and anti-platelet effects. Here we have to present a static and a dynamic view for the pretended aspirin bioreactor
Rayane Dergham, Hind Abd El Hamid @ MEGBI/ AECENAR November 2022
www.aecenar.com
Pilot Plant Scale for Aspirin Production
Tank2
Tank1
Tank3
Tank6
1- Tank 1 :
Place 1013.5g of salicylic acid
Add 2.5L acetic anhydride
Add 125ml concentrated H2SO4
Mix and heat to 85º for at least 10min .
2- Tank 2 :
Open valve V1/2
Cool down the mix to between 25- 28º.
3- Tank 3 to tank 2 :
Open Valve V3/2
Add 5L warm water .
4- Tank 2 to tank 4
Open valve V2/4
Cool the mix about 20min in an ice bath with mixing .
Crystals are formed now.
5- Tank 4 to tank 5:
Open valve V4/5 V5 and V5/6
let the vacuum filtration begin.
Aspirin crystals are now into the filter paper in tank 5.
6- Filtrate discarding:
Open valve V6/out
The filtrate is discarded from the tank 6 out of the system
Close valve V5, V6/out, and V5/6
7- Tank 5:
Open valve V3/5
The obtained aspirin crystals are re-dissolved with 30L warm water for about 20 min.
Open valve V5 and valve V5/7
8- Tank 7 to 4:
Open valve V7/4
The solution is pumped now from tank 7 to tank 4 for the second crystallization.
9-Tank 4:
Re-cool the mix about 20 min in the ice bath with mixing.
Open valve V4/5 for the final vacuum filtration.
10-Tank 6 :
Open valve V5/6 and V6/out
Crude Aspirin crystals are harvested from tank 5 and ready to be dry, tested and compressed for market.
11- Sterilization:
Close all the valves
The whole system must be sterilized by using sterilizer system
The valves are successively re-opened as mentioned as above.
Figure 2 : The real Aspirin production system
Figure 1 : An approximative view of aspirin system production
Sterilizer